## Slide 1: Industry Briefing for Sunday 2 TT May 2023
Monday 15th August 2022, Presented by Anna Scannell, Nicholas Hewett and Jacob Delin

## Slide 2: Agenda
Introductions- Anna Scannell
Meeting Purpose- Anna Scannell
GWML Sunday demand forecasts- Jacob Delin
Service Specification- Nicholas Hewett
Open Discussion- All
Next Steps- Anna Scannell
Close

## Slide 3: Service specification
Inputs and Assumptions

## Slide 4: Key Inputs and Assumptions
Maximum capacity during a block is 14.5tph
During a Relief Line block, up to 2tph could be run to/from Old Oak Common Elizabeth Line depot
Westbourne Park can turn back in excess of 12tph, but not the full minimum 20tph EL Sunday service on a sustained basis
No consideration is given to destinations beyond Reading, recognising wider specification may differ by date
On train capacity is as follows
  GWR – 9-car 800: 650 passengers
  Elizabeth Line – 345: 1500 passengers. This is halved for airport traffic (as an approximation)
  Heathrow Express – 387: 200 passengers

## Slide 5: Methodology
The hour with the highest forecast was chosen from each direction noting:
The split of demand between the four operations is broadly similar across the day
Across the central 10-hour period on a Sunday, demand fluctuates between 4-7,000 arrivals per hour
Highest variances were early morning/ late evening – further trade-offs may be made to handle fluctuations
The DfT DDG growth forecast for 2026 is used, moderated with Railplan data
The demand for passengers traveling to/from Paddington is allocated first proportionally, and then by on-train capacity to produce potential specifications with train loadings. Airport passengers may be reallocated between operators considering the geographic overlap in service offering
GWR may target a lower on-train capacity due to variation in origin-destination pairs

## Slide 6: Potential split – A. Current
A roll-forward of previous practice with a 6.5/4/4 split shows the following issues:
GWR capacity becoming constrained
EL capacity of 450 seats/train an issue
Significant under provision on Heathrow Airport market
High discrepancy between overall loadings on different operators/routes
Up Direction |  |  |  |  |  |  |  | 
Operator | Pax no | Pax split | Carrying capacity | Route capacity | Allocation split | Capacity allocated | Train loadings | % Capacity
GW Reliefs | 915 | 7.42% | 450 | 14.5 | 1.1 | 2 | 457.72 | 101.72%
GW Mains | 4454 | 36.12% | 650 | 14.5 | 5.2 | 6.5 | 685.30 | 105.43%
Heathrow Express | 276 | 2.24% | 374 | 14.5 | 0.3 | 4 | 69.01 | 18.45%
Heathrow EL | 1261 | 10.22% | 450 | 14.5 | 1.5 | 2 | 630.30 | 140.07%
Down Direction |  |  |  |  |  |  |  | 
Operator | Pax no | Pax split | Carrying capacity | Route capacity | Allocation split | Capacity allocated | Train loadings | % Capacity
GW Reliefs | 627 | 5.08% | 450 | 14.5 | 0.7 | 2 | 313.44 | 69.65%
GW Mains | 3622 | 29.37% | 650 | 14.5 | 4.3 | 6.5 | 557.23 | 85.73%
Heathrow Express | 343 | 2.79% | 374 | 14.5 | 0.4 | 4 | 85.87 | 22.96%
Heathrow EL | 2250 | 18.24% | 450 | 14.5 | 2.6 | 2 | 1124.79 | 249.95%

## Slide 7: Potential split – B. Reduce HEX to 2tph
Reallocation of 2 HEX paths to Elizabeth Line or GWR. Increasing GWR to 8.5tph provides adequate capacity on long distance services but leaves the Heathrow market underprovided. Increasing EL paths to Heathrow to 4tph would resolve the problem for airport customers, but leave the GWR long-distance challenge in place
Up direction |  |  |  |  |  |  |  | 
Operator | Pax no | Pax split | Carrying capacity | Route capacity | Allocation split | Capacity allocated |  | 
GW Reliefs | 915 | 7.42% | 450 | 14.5 | 1.1 | 2 | 457.72 | 101.72%
GW Mains | 4454 | 36.12% | 650 | 14.5 | 5.2 | 6.5 | 685.30 | 105.43%
Heathrow Express | 276 | 2.24% | 374 | 14.5 | 0.3 | 2 | 138.02 | 36.90%
Heathrow EL | 1261 | 10.22% | 450 | 14.5 | 1.5 | 4 | 315.15 | 70.03%
Up Direction |  |  |  |  |  |  |  | 
Operator | Pax no | Pax split | Carrying capacity | Route capacity | Allocation split | Capacity allocated |  | 
GW Reliefs | 915 | 7.42% | 450 | 14.5 | 1.1 | 2 | 457.72 | 101.72%
GW Mains | 4454 | 36.12% | 650 | 14.5 | 5.2 | 8.5 | 524.06 | 80.62%
Heathrow Express | 276 | 2.24% | 374 | 14.5 | 0.3 | 2 | 138.02 | 36.90%
Heathrow EL | 1261 | 10.22% | 450 | 14.5 | 1.5 | 2 | 630.30 | 140.07%
Down Direction |  |  |  |  |  |  |  | 
Operator | Pax no | Pax split | Carrying capacity | Route capacity | Allocation split | Capacity allocated |  | 
GW Reliefs | 627 | 5.08% | 450 | 14.5 | 0.7 | 2 | 313.44 | 69.65%
GW Mains | 3622 | 29.37% | 650 | 14.5 | 4.3 | 6.5 | 557.23 | 85.73%
Heathrow Express | 343 | 2.79% | 374 | 14.5 | 0.4 | 2 | 171.73 | 45.92%
Heathrow EL | 2250 | 18.24% | 450 | 14.5 | 2.6 | 4 | 562.39 | 124.98%
Down direction |  |  |  |  |  |  |  | 
Operator | Pax no | Pax split | Carrying capacity | Route capacity | Allocation split | Capacity allocated |  | 
GW Reliefs | 627 | 5.08% | 450 | 14.5 | 0.7 | 2 | 313.44 | 69.65%
GW Mains | 3622 | 29.37% | 650 | 14.5 | 4.3 | 8.5 | 426.12 | 65.56%
Heathrow Express | 343 | 2.79% | 374 | 14.5 | 0.4 | 2 | 171.73 | 45.92%
Heathrow EL | 2250 | 18.24% | 450 | 14.5 | 2.6 | 2 | 1124.79 | 249.95%

## Slide 8: Potential split – C. HEX does not operate
NB: HEX demand reallocated to Elizabeth Line Heathrow services
Airport demand handled at 4tph provided higher capacity EL services used; 6 tph potentially overproviding
Up Direction |  |  |  |  |  |  |  | 
Operator | Pax no | Pax split | Carrying capacity | Route capacity | Allocation split | Capacity allocated |  | 
GW Reliefs | 915 | 7.42% | 450 | 14.5 | 1.1 | 2 | 457.72 | 101.72%
GW Mains | 4454 | 36.12% | 650 | 14.5 | 5.2 | 6.5 | 685.30 | 105.43%
Heathrow Express | 0 | 0.00% | 374 | 14.5 | 0.0 | 0 | 0.00 | 0.00%
Heathrow EL | 1537 | 12.46% | 450 | 14.5 | 1.8 | 6 | 256.11 | 56.91%
Up Direction |  |  |  |  |  |  |  | 
Operator | Pax no | Pax split | Carrying capacity | Route capacity | Allocation split | Capacity allocated |  | 
GW Reliefs | 915 | 7.42% | 450 | 14.5 | 1.1 | 2 | 457.72 | 101.72%
GW Mains | 4454 | 36.12% | 650 | 14.5 | 5.2 | 8.5 | 524.06 | 80.62%
Heathrow Express | 0 | 0.00% | 374 | 14.5 | 0.0 | 0 | 0.00 | 0.00%
Heathrow EL | 1537 | 12.46% | 450 | 14.5 | 1.8 | 4 | 384.16 | 85.37
Down Direction |  |  |  |  |  |  |  | 
Operator | Pax no | Pax split | Carrying capacity | Route capacity | Allocation split | Capacity allocated |  | 
GW Reliefs | 627 | 5.08% | 450 | 14.5 | 0.7 | 2 | 313.44 | 69.65%
GW Mains | 3622 | 29.37% | 650 | 14.5 | 4.3 | 6.5 | 557.23 | 85.73%
Heathrow Express | 0 | 0.00% | 374 | 14.5 | 0.0 | 0 | 0.00 | 0.00%
Heathrow EL | 2593 | 21.03% | 450 | 14.5 | 3.0 | 6 | 432.17 | 96.04%
Down Direction |  |  |  |  |  |  |  | 
Operator | Pax no | Pax split | Carrying capacity | Route capacity | Allocation split | Capacity allocated |  | 
GW Reliefs | 627 | 5.08% | 450 | 14.5 | 0.7 | 2 | 313.44 | 69.65%
GW Mains | 3622 | 29.37% | 650 | 14.5 | 4.3 | 8.5 | 426.12 | 65.56%
Heathrow Express | 0 | 0.00% | 374 | 14.5 | 0.0 | 0 | 0.00 | 0.00%
Heathrow EL | 2593 | 21.03% | 450 | 14.5 | 3.0 | 4 | 648.26 | 144.06%

## Slide 9: Priorities for Concept Train Plan Development
Key findings:
  Need to uplift airport capacity overall
  GWR long distance capacity also a challenge
  EL services to Reading providing more than enough with 2tph, but is a reduction viable?
  Are further tweaks available between Airport Junction and Reading to better prioritise passengers?
Existing split not under active development as already understood, and not reflective of passenger demand
14.5 tph priority concept of 6.5/2/6 under development to redress airport shortfall (no further detriment to GWR)
Need to look at specifications removing inner Thames Valley calls to raise capacity above 14.5tph - e.g. if all trains are non-stop, could more be accommodated robustly
Need to look at wider system demand levels to maximise value of the 6.5tph GWR allocation and any available mitigations
Will need to factor in performance assessments of changes