## Slide 1
Sheepcote RRAP
Justifications & benefits

## Slide 2
Road Rail Access Point Context at Clapham Jn
Clapham TME area, hamstrung by lack of RRAPs
Only 1 x purpose built facility at Covent Garden but this not usable for more than half of possession templates
On Windsor side:
  Police Compound: capacity is very low and access takes a minimum of 1 week to arrange
  Vine Rd: where road closure must be booked and is over 7 miles from Waterloo

## Slide 3
Alternatives to RRVs
Lack of RRAPs necessitates reliance on excessive usage on Plasser 12t Rail Cranes which were built for British Rail in 1970s and cost £3850 per shift to hire from sole supplier Balfour Beatty
Unsurprisingly given their age, the reliability of these cranes is poor and they are approaching their operational life expiry in the coming years
There is currently no planned replacement for
these machines when they finally go out of service
Competencies for operating and controlling
GPCs are rare and cancellations due to lack of
competent drivers or crane controllers is
extremely common
Due to the limited number of these cranes still
in service and very small pool of competent
trainers, training new staff

## Slide 4
Safety impact of lack of level access points
Waterloo – Clapham corridor built up on brick viaducts meaning that generally all forms of access (not just RRAPs) are rare
Handful of pedestrian access points that do exist require staff to manually carry heavy loads (1000kg+ for welding kit) up staircases
RRAPs like the sheepcote proposal would therefore also allow staff to load equipment on a level surface
This provides a general safety improvement even when RRVs are not being used at a RRAP site

## Slide 5
Sheepcote Lane RRAP proposal
Sheepcote lane offers a unique opportunity to improve NR’s ability to maintain and renew the railway around Clapham Jn
Positioned on an essentially disused line, where the only regularly scheduled train is a 3 monthly track recording path, works can be undertaken without impact on passengers and freight
Location is the last earth embankment prior to the brick viaduct approaching Waterloo and therefore a ramp can be constructed from sheet piles for circa £850k.
As a comparison, in 2012 Covent Garden RRAP which was constructed by building up an access ramp next to a brick viaduct cost £3m
The Sheepcote Curves also contain the route boundary between Wessex & Sussex, which means the facility will benefit both routes

## Slide 6
Sheepcote Lane Pre-planned Capital Works
Sheepcote lane is already pre-planned as a critical element in CP7 works
The most prominent examples is for Christmas 2025 where the facility is planned to allow works to be undertaken S&C renewal of 607A/B, 608A/B, 609A/B, 610s & 1790s at Queenstown Road, along with a plain line renewal of platform 2 there and S&C refurbishment of 1600/1601pts at Vauxhall
This work has been planned for this Christmas and cannot fit anywhere else in CP7 because of the impact of HS2 and Old Oak Common works which will require Waterloo station to be undisrupted for all other Christmas periods